## Slide 1: Serbian Danish District Heating Days Vrnjačka Banja, Serbia – 18 to 20 April 2023 Green transition of the district heating sector – including surplus heat from data centers
Lars Gullev
Senior consultant
Vice-chair, IEA DHC
Zlatiborski – 19 April 2017

## Slide 2: Agenda
Paris Agreement
CO2-emission in Serbia and Denmark
VEKS Strategy and CO2-emission
Impact points
  Storage
  Data center
  Carbon Capture (CC)
Summary

## Slide 3: Agenda
Paris Agreement
CO2-emission in Serbia and Denmark
VEKS Strategy and CO2-emission
Impact points
  Storage
  Data center
  Carbon Capture (CC)
Summary

## Slide 4: Paris Agreement A global challenge and a global agreement
In 2015, 196 countries signed the UN's major climate agreement in Paris.
Together they set a goal:
  Prevent the global temperature from rising by more than 2 degrees C.
The countries committed to share their national climate action plans and say how much they want to reduce their greenhouse gas emissions - but it is voluntary whether they actually do it!

## Slide 5: Paris Agreement A global challenge and a global agreement
The EU has announced, on behalf of Denmark and the other EU countries, that we will collectively reduce our emission of greenhouse gases by 55% in 2030 compared to the level in 1990.
The EU's climate policy is about achieving that goal.
The EU was founded as a community for coal and steel. Today, it is a main priority to reduce CO2 pollution.

## Slide 6: Agenda
Paris Agreement
CO2-emission in Serbia and Denmark
VEKS Strategy and CO2-emission
Impact points
  Storage
  Data center
  Carbon Capture (CC)
Summary

## Slide 7: Development in CO2 emissions Serbia and Denmark
Political decision in Denmark:
  CO2-emission in 2030 must be reduced by 70% compared to the 1990-level.
Development 2000-2019
  Serbia Plus 13%
  Denmark Minus 48%
Chart: Annual CO2-emission – ton/inhabitant
| Serbia | Denmark
2000 | 5.85 | 9.85
2019 | 6.62 | 5.11
Source: CO2-udslip per indb. (globalis.dk)
Source: CO2 emissions (metric tons per capita) | Data (worldbank.org)

## Slide 8: Agenda
Paris Agreement
CO2-emission in Serbia and Denmark
VEKS Strategy and CO2-emission
Impact points
  Storage
  Data center
  Carbon Capture (CC)
Summary

## Slide 10: Carbon footprint
Reduction from 1990-level
83.5%

## Slide 11
Sustainable biomass
Waste-to-heat
Test, large scale heat pumps
Test, thermal heat storage
Large heat pumps
Thermal heat storage
Surplus heat from datacentres
Low temperature
Test, geothermal energy
AI and AM
Large heat pumps
Surplus heat from datacentres and industry
CHP (AVV2)
Geothermal
Low temperature
Large heat pumps
Surplus heat from datacentres and industry
Decommissioning CHP (AVV)
Geothermal
Low temperature
Power to X and Carbon capture
Decentralised heat production

## Slide 12: Impact point
Storage

## Slide 13: Thermal storages - Four concepts

## Slide 14: Design concept of the PTES Modelling of the PTES as part of the total heating system
Heat storage plant
The PTES receives heat from the transmission network (TF~ 95-1100C) and delivers heat to the distribution network (TF ~ 750C).
The local production is operated such that it does not prevent discharge of the storage.

## Slide 15: PTES in Taastrup Construction works started 2020 Went into operation February 2023
Data for PTES
Volume: 70,000 m3
Energy content: 3,300 MWh
L/W/H: 179 m/55-69 m/ 14.5 m
Annual CO2-reduction: 10-15,000 tons

## Slide 16: Heatlosses from PTES (60,000 m3) Dronninglund, DK - 2014-2016
10,5 %

## Slide 17: PTES under construction

## Slide 18
PTES in Taastrup – August 2022
6,000 bags – each 12.5 kg

## Slide 19: Cover
New cover solution from Aalborg CSP (used in Marstal, DK – photo).
Built on floating plastic liner.
Modular solution to minimise maintenance.
The cover is to divert rainwater and diffuse steam through a float liner – and is going to insulate against heat loss.

## Slide 20: Impact point
Data center

## Slide 21
In the future DH in Odense, DK, will be green and flexible
Central
Decentral
Carbon Capture (CCS)
Power-to-X (PtX)
TBV: Tietgenbyens Varme Central (heat pumps near facebook)
EMV: Ejby Mølle Varme Central (heat pumps utilizing sewage sluge

## Slide 22: Facts about the Meta/Facebook heat recovery project
22
Facts:
Data center owned and operated by Facebook
Heat pump plant owned and operated by Fjernvarme Fyn
Both facilities supplied by renewable energy
Facts:
160,000 MWh surplus heat ~ 11,000 households
2017: Investment decision
2020-2021: Commissioning of TBV1 and TBV2

## Slide 23: Expansion of Meta and Tietgenbyen heat central (TBV)
23
Source: Facebook and Fjernvarme Fyn
Phase one (2020)
Facebook: 2 data buildings (ODN 1+2)
Fjernvarme Fyn: 25 MW heat pumps (TBV 1)
Agreement: 100.000 MWh surplus heat ~ 6,900 households
Phase two (2021)
Facebook: + 1 data building (ODN 3)
Fjernvarme Fyn: + 20 MW heat pumps (TBV 2)
Agreement: + 60.000 MWh surplus heat ~ 4000 households
2023
Continuous optimization of surplus heat utilization

## Slide 24: Situation map of heat pumps and data center Tietgenbyen, Odense SØ, DK
Heat Pumps
Tietgenbyens Varme Central (TBV)
Odense Data Center
Facebook
Low temperature district heating grid
Fraugde transformer station
Characteristics of DK system:
High security of supply
High RES
Stable data

## Slide 25: Impact point
Carbon Capture

## Slide 26: What is C4 (Carbon Capture Cluster Copenhagen)? A consortium of nine companies established December 2020
Waste-to energy plants
  ARC, ARGO and Vestforbrænding
Watertreatment plant
  BIOFOS
Biomassbased CHP plants
  HOFOR (BIO4-plant) and Ørsted (AVV)
DH transmission companies
  CTR and VEKS
Port
  CMP (Copenhagen and Malmö Port)

## Slide 27: What is the goal for C4?
To make carbon capture (CC) a crucial element in the green transition in Denmark.
CO2 reductions of around 3 million tons/year are possible among the partners of C4.
3 million tons are approx. 15% of the total Danish target for reduction of 70% by the year 2030 and could be one of the largest single contributions to the green transition in Denmark.
3 million tons/year

## Slide 28
Avedøre CHP Plant, Copenhagen DK Unit 1 (1990/2016) and unit 2 (2001/2014)
Straw-unit
Unit 2
Unit 1
Heat storage
Storage for wood pellets
100 % sustainable biomass - 856 MJ/s heat

## Slide 29: Avedøre CHP Plant – Surplus heat from CC and PtX

## Slide 30: Agenda
Paris Agreement
CO2-emission in Serbia and Denmark
VEKS Strategy and CO2-emission
Impact points
  Storage
  Data center
  Carbon Capture (CC)
Summary

## Slide 31: Summary
Both Data Centers, Carbon Capture process and the Power-to-X process generate large amounts of excess heat….
Notes: 18-04-2023
31

## Slide 32: Summary
Only a society with a well-functioning district heating system can make optimal use of the energy resources of the future.
Without DH the resources would be lost for the society.
Notes: 18-04-2023
32

## Slide 33
Thank you
Further information:
www.veks.dk
lg@veks.dk
Thermal storage, Iceland